## Slide 1: General Licensing Class
G9A – G9D
Antennas
Your organization and dates here
Notes: 1

## Slide 2: General Class Element 3 Course Presentation
ELEMENT 3 SUB-ELEMENTS
  G1 – Commission’s Rules
  G2 – Operating Procedures
  G3 – Radio Wave Propagation
  G4 – Amateur Radio Practices
  G5 – Electrical Principles
  G6 – Circuit Components
  G7 – Practical Circuits
  G8 – Signals and Emissions
  G9 – Antennas
  G0 – Electrical and RF Safety

## Slide 3: Antennas
The distance between the centers of the conductors and the radius of the conductors determine the characteristic impedance of a parallel conductor antenna feed line. (G9A01)
50 and 75 ohms are the typical characteristic impedances of coaxial cables used for antenna feed lines at amateur stations. (G9A02)
300 Ohm Twin Lead
Air Dielectric Coaxial Cable
Parallel two-wire line

## Slide 4: Antennas
300 ohms is the characteristic impedance of flat ribbon TV type twinlead. (G9A03)
A difference between feed-line impedance and antenna feed-point impedance is the reason for the occurrence of reflected power at the point where a feed line connects to an antenna. (G9A04)
The attenuation of coaxial cable increases as the frequency of the signal it is carrying increases. (G9A05)
RF feed line losses usually expressed in dB per 100 ft. (G9A06)

## Slide 5: Antennas

## Slide 6: Antennas
To prevent standing waves on an antenna feed line, the antenna feed-point impedance must be matched to the characteristic impedance of the feed line. (G9A07)
If the SWR on an antenna feed line is 5 to 1, and a matching network at the transmitter end of the feed line is adjusted to 1 to 1 SWR, the resulting SWR on the feed line is still 5 to 1. (G9A08)
    The antenna tuner allows the transmitter to see a matched impedance
    This delivers full power.
    It does not change the antenna or feedline impedance on its output.
Antenna tuner with built in dual needle SWR meter

## Slide 7: Antennas
A 4:1 standing wave ratio will result from the connection of a 50-ohm feed line to a non-reactive load having a 200-ohm impedance. (G9A09)
A standing wave ratio of 5:1 will result from the connection of a 50-ohm feed line to a non-reactive load having a 10-ohm impedance. (G9A10)
SWR = Z1 / Z2
200/ 50
4:1 VSWR
SWR = Z1 / Z2
50/ 10
5:1 VSWR

## Slide 8: Antennas
A standing wave ratio of 1:1 will result from the connection of a 50-ohm feed line to a non-reactive load having a 50-ohm impedance. (G9A11)
SWR = Z1 / Z2
50 / 50
1 : 1 VSWR

## Slide 9: Antennas
If you feed a vertical antenna that has a 25-ohm feed-point impedance with 50-ohm coaxial cable, the SWR will be 2:1. (G9A12)
If you feed an antenna that has a 300-ohm feed-point impedance with 50-ohm coaxial cable, the SWR will be 6:1. (G9A13)
One disadvantage of a directly fed random-wire antenna is that you may experience RF burns when touching metal objects in your station. (G9B01)
    As the name implies, random-wire antennas are a random-length.
    To match the antenna to the transmitter, you’ll need an antenna tuner
    Because of this, there may be high RF levels in the shack when you are transmitting.
50 / 25
2:1 VSWR
SWR = Z1 / Z2
SWR = Z1 / Z2
300/ 50
6:1 VSWR

## Slide 10: Antennas
An advantage of downward sloping radials on a quarter wave ground-plane antenna is that they bring the feed-point impedance closer to 50 ohms. (G9B02)
The natural feed point of a quarter-wave vertical is 35 ohms, but the feed-point impedance of a ground-plane antenna increases when its radials are changed from horizontal to downward-sloping. (G9B03)
  Bending the radials changes the impedance up towards 50 ohms.
Notice ground plane elements are angled downwards.

## Slide 11: Antennas
The low angle azimuthal radiation pattern of an ideal half-wavelength dipole antenna installed 1/2 wavelength high and parallel to the Earth is a figure-eight at right angles to the antenna. (G9B04)
If the antenna is less than 1/2 wavelength high, the azimuthal pattern is almost omnidirectional and maximum straight up. (G9B05)
Omni-directional pattern
Patterns change as height above ground is varied

## Slide 12: Antennas
The radial wires of a ground-mounted vertical antenna system should be placed on the surface or buried a few inches below the ground. (G9B06)
Ground wire kit.
Surface mounted ground wires.
Calculate ½ wavelength in feet by dividing 468 by the frequency in MHz.
468/28.5
16.4 Feet
A ¼ wave antenna would be ½ the length of a ½ wave antenna
16.4/2
8.2 Feet

## Slide 13: Antennas
As the antenna is lowered from 1/4 wave above ground, the feed-point impedance of a 1/2 wave dipole antenna steadily decreases. (G9B07)
  Antenna height affects the feed point impedance.
The feed-point impedance of a 1/2 wave dipole steadily increases as the feed-point location is moved from the center toward the ends. (G9B08)

## Slide 14: Antennas
An advantage of a horizontally polarized as compared to vertically polarized HF antenna is lower ground reflection losses. (G9B09)
  Propagation via multi-hop refraction:
    RF energy is lost each time the radio wave is reflected from the Earth's surface.
  The amount of energy lost depends on:
    Frequency of the wave
    Angle of incidence
    Ground irregularities
    Electrical conductivity of the point of reflection.

## Slide 15: Antennas
32 feet is the approximate length for a 1/2-wave dipole antenna cut for 14.250 MHz. (G9B10)
    Calculate ½ wavelength in feet by dividing 468 by the frequency in MHz.
    468 / 14.250
    32.8 Feet
The approximate length for a 1/2-wave dipole antenna cut for 3.550 MHz is 131 feet. (G9B11)
    Calculate ½ wavelength in feet by dividing 468 by the frequency in MHz.
    468 / 3.550 or
    131.8 Feet
Half-wave Dipole with 450 ohm feedline (not coax).

## Slide 16: Antennas
The approximate length for a 1/4-wave vertical antenna cut for 28.5 MHz is 8 feet. (G9B12)
Calculate ½ wavelength in feet by dividing 468 by the frequency in MHz.
468/28.5
16.4 Feet
A ¼ wave antenna would be ½ the length of a ½ wave antenna
16.4/2
8.2 Feet

## Slide 17: Antennas
Larger diameter elements increase the bandwidth of a Yagi antenna. (G9C01)
The approximate length of the driven element of a Yagi antenna is 1/2 wavelength. (G9C02)
In a three-element, single-band Yagi antenna, the director is normally the shortest parasitic element. (G9C03)
The reflector is normally the longest parasitic element of a three-element, single-band Yagi antenna. (G9C04)

## Slide 18: Antennas
The gain increases when you increase boom length and add directors to a Yagi antenna. (G9C05)
A Yagi antenna is often used for radio communications on the 20 meter band because it helps reduce interference from other stations to the side or behind the antenna. (G9C06)

## Slide 19: Antennas
The "front-to-back ratio" of a Yagi antenna is the power radiated in the major radiation lobe compared to the power radiated in exactly the opposite direction. (G9C07)
The “major lobe” or "main lobe" of a directive antenna is the direction of maximum radiated field strength from the antenna. (G9C08)

## Slide 20: Antennas
The approximate maximum theoretical forward gain of a three element, single-band Yagi antenna is 9.7 dBi. (G9C09)
  dBi refers to a reference level of dB Isotropic
  which is the signal strength from an ideal point source of energy
  that radiates equally in all directions in a sphere surrounding the point RF source.
  Isotropic radiators are used as reference radiators
  An isotropic radiator is a theoretical point source of electromagnetic or sound waves.

## Slide 21: Antennas
In a Yagi antenna design, the following variables that could be adjusted to optimize forward gain, front-to-back ratio, or SWR bandwidth (G9C10)
  The physical length of the boom
  The number of elements on the boom
  The spacing of each element along the boom
All of these choices are correct

## Slide 22: Antennas
The purpose of a gamma match used with Yagi antennas is to match the relatively low feed-point impedance to 50 ohms. (G9C11)
An advantage of using a gamma match for impedance matching of a Yagi antenna to 50-ohm coax feed line is that it does not require that the elements be insulated from the boom. (G9C12)

## Slide 23: Antennas
The elements of a quad antenna are square loops. Each side of a quad antenna driven element is approximately 1/4 wavelength. (G9C13)
Driven Element for each side (in feet) =
1005
f (MHz)
/
4
Horizontal polarization feed-point

## Slide 24: Antennas
The forward gain of a two-element quad antenna is about the same as the forward gain of a three-element Yagi antenna. (G9C14)
Each side of a quad antenna reflector element is slightly more than 1/4 wavelength. (G9C15)

## Slide 25: Antennas
The gain of a two-element delta-loop beam is about the same as the gain of a two-element quad antenna. (G9C16)
Each leg of a symmetrical delta-loop antenna is approximately 1/3 wavelength. (G9C17)
Driven Element for each side (in feet) =
1005
f (MHz)
3
/

## Slide 26: Antennas
The polarization of the radiated signal changes from horizontal to vertical when the feed point of a quad antenna is changed from the center of the either horizontal wire to the center of either vertical wire. (G9C18)
The reflector element must be approximately 5% longer than the driven element for a two-element quad antenna when the antenna is meant to operate as a beam antenna, assuming one of the elements is used as a reflector. (G9C19)
Yagi antennas spaced vertically 1/2 wavelength apart typically is approximately 3 dB higher than the gain of a single 3-element Yagi. (G9C20)

## Slide 27: Antennas
The term "NVIS" means Near Vertical Incidence Sky wave when related to antennas. (G9D01)
An advantage of an NVIS antenna is high vertical angle radiation for working stations within a radius of a few hundred kilometers. (G9D02)
Angle of radiation determines the area of coverage

## Slide 28: Antennas
An NVIS antenna typically installed between 1/10 and 1/4 wavelength above ground. (G9D03)
The primary purpose of antenna traps is to permit multiband operation. (G9D04)

## Slide 29: Antennas
The advantage of vertical stacking of horizontally polarized Yagi antennas is that it narrows the main lobe in elevation. (G9D05)
Vertical Stacking of Horizontally polarized.
Horizontal Stacking of Vertically polarized.

## Slide 30: Antennas
The gain of a log periodic antenna is less than that of a Yagi, but an advantage of a log periodic antenna is wide bandwidth. (G9D06)
For a log periodic antenna, the length and spacing of the elements increases logarithmically from one end of the boom to the other. (G9D07)
290 – 2000 MHz
0.15 – 300 MHz
EW8DQ, and his rotatable HF log-periodic beam antenna in Belarus

## Slide 31: Antennas
A Beverage antenna is not used for transmitting because it has high losses compared to other types of antennas. (G9D08)
An application for a Beverage antenna is as a directional receiving for low HF bands. (G9D09)
A Beverage antenna is a very long and low directional receiving antenna. (G9D10)

## Slide 32: Antennas
A disadvantage of multiband antennas is that they have poor harmonic rejection. (G9D11)
Hex Wire Beam multi band
Five band beam 20‑10m